## Slide 1
Chapter 4 ARM Assembly Language
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
1

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: ARM Assembly Language
One of the most popular RISC instruction sets in use today
Used by licensees of ARM Limited, UK
  ARM processors
  Some processors by Samsung, Qualcomm, and Apple
Highly versatile instruction set
  Floating-point and vector (multiple operations per instruction) extensions

## Slide 4: Outline
Basic Instructions
Advanced Instructions
Branch Instructions
Memory Instructions
Instruction Encoding

## Slide 5: ARM Machine Model
16 registers – r0 … r15
  The PC is explicitly visible
Memory (Von Neumann Architecture)
Register
Abbrv.
Name
r11
fp
frame pointer
r12
ip
intra-procedure-call scratch register
r13
sp
stack pointer
r14
lr
link register
r15
pc
program counter

## Slide 6: Data Transfer Instructions
mov and mvn (move not)
Semantics
Example
Explanation
mov reg, (reg/imm)
mov r1, r2
r1 ← r2
mov r1, #3
r1 ← 3
mvn r1, r2
r1 ← ∼ r2
mvn r1, #3
r1 ← ∼ 3
mvn reg, (reg/imm)

## Slide 7: Arithmetic Instructions
add, sub, rsb (reverse subtract)
Semantics
Example
Explanation
add reg, reg, (reg/imm)
sub reg, reg, (reg/imm)
rsb reg, reg, (reg/imm)
add r1, r2, r3
sub r1, r2, r3
rsb r1, r2, r3
r1 ← r2 + r3
r1 ← r2 - r3
r1 ← r3 - r2

## Slide 8: Example
Write an ARM assembly program to compute: 4+5 - 19. Save the result in
r1.
Answer: Simple yet suboptimal solution.
mov r1, #4
mov r2, #5
add r3, r1, r2
mov r4, #19
sub r1, r3, r4
Optimal solution.
mov r1, #4
add r1, r1, #5
sub r1, r1, #19

## Slide 9: Logical Instructions
and, eor (exclusive or), orr (or), bic(bit clear)
Semantics
and reg, reg, (reg/imm)
eor reg, reg, (reg/imm)
orr reg, reg, (reg/imm)
bic reg, reg, (reg/imm)
Example
and r1, r2, r3
eor r1, r2, r3
orr r1, r2, r3
bic r1, r2, r3
Explanation
r1 ← r2 AND r3
r1 ← r2 XOR r3
r1 ← r2 OR r3
r1 ← r2 AND (∼ r3)

## Slide 10: Example
Write an ARM assembly program to compute:, where A and B are 1 bit Boolean values. Assume that A = 0 and B = 1. Save the result in r0.
Answer:
mov r0, #0x0
orr r0, r0, #0x1
mvn r0, r0

## Slide 11: Multiplication Instruction
smull and umull instructions can hold a 64 bit operand
Semantics
mul reg, reg, (reg/imm)
mla reg, reg, reg, reg
smull reg, reg, reg, reg
umull reg, reg, reg, reg
Example
mul r1, r2, r3
mla r1, r2, r3, r4
smull r0, r1, r2, r3
umull r0, r1, r2, r3
Explanation
r1 ← r2 × r3
r1 ← r2 × r3 + r4
r1 r0← r2 ×signed r3
64
r1 r0← r2 ×unsigned r3
64

## Slide 12: Example
Compute 123 + 1, and save the result in r3.
Answer:
/* load test values */
mov r0, #12
mov r1, #1
/* perform the logical computation */
mul r4, r0, r0 @ 12*12
mla r3, r4, r0, r1 @ 12*12*12 + 1

## Slide 13: Outline
Basic Instructions
Advanced Instructions
Branch Instructions
Memory Instructions
Instruction Encoding

## Slide 14: Shifter Operands
reg1
,
lsl
lsr
asr
ror
#shift_amt
reg2
1 0 1 1 0
lsl #1
0 1 1 0 0
1 0 1 1 0
lsr #1
0 1 0 1 1
Generic format
1 0 1 1 0
asr #1
1 1 0 1 1
1 0 1 1 0
ror #1
0 1 0 1 1
Examples

## Slide 15: Examples of Shifter Operands
Write ARM assembly code to compute: r1 = r2 / 4.
Answer:
mov r1, r2, asr #2
Write ARM assembly code to compute: r1 = r2 + r3 × 4.
Answer:
add r1, r2, r3, lsl #2

## Slide 16: Compare Instructions
Sets the flags of the CPSR register
  CPSR (Current Program Status Register)
  N (negative) , Z (zero), C (carry), F (overflow)
  If we need to borrow a bit in a subtraction, we set C to 0, otherwise we set it to 1.
Semantics
cmp reg, (reg/imm)
cmn reg, (reg/imm)
tst reg, (reg/imm)
teq reg, (reg/imm)
Example
cmp r1, r2
cmn r1, r2
tst r1, r2
teq r1, r2
Explanation
Set flags after computing (r1 - r2)
Set flags after computing (r1 + r2)
Set flags after computing (r1 AND r2)
Set flags after computing (r1 XOR r2)

## Slide 17: Instructions with the 's' suffix
Compare instructions are not the only instructions that set the flags.
We can add an s suffix to regular ALU instructions to set the flags.
  An instruction with the 's' suffix sets the flags in the CPSR register.
  adds (add and set the flags)
  subs (subtract and set the flags)

## Slide 18: Instructions that use the Flags
add and subtract instructions that use the value of the carry flag
Semantics
adc reg, reg, reg
sbc reg, reg, reg
rsc reg, reg, reg
Example
adc r1, r2, r3
sbc r1, r2, r3
rsc r1, r2, r3
Explanation
r1 = r2 + r3 + Carry Flag
r1 = r2 - r3 - NOT(Carry Flag)
r1 = r3 - r2 - NOT(Carry Flag))

## Slide 19: 64 bit addition using 32 bit registers
Add two long values stored in r2,r1 and r4,r3.
Answer:
adds r5, r1, r3
adc r6, r2, r4
The (adds) instruction adds the values in r1 and r3. adc(add with carry) adds r2, r4, and the value of the carry flag. This is exactly the same as normal addition.

## Slide 20: Outline
Basic Instructions
Advanced Instructions
Branch Instructions
Memory Instructions
Instruction Encoding

## Slide 21: Simple Branch Instructions
b (unconditional branch)
b<code> (conditional branch)
Semantics
b label
beq label
bne label
Example
b .foo
beq .foo
bne .foo
Explanation
Jump unconditionally to label .foo
Branch to .foo if the last flag setting
instruction has resulted in an equality
and (Z flag is 1)
Branch to .foo if the last flag setting
instruction has resulted in an inequality
and (Z flag is 0)

## Slide 22: Branch Conditions
Number
Suffix
Meaning
Flag State
0
eq
equal
Z = 1
1
ne
notequal
Z = 0
2
cs/hs
carry set/ unsigned higher or equal
C = 1
3
cc/lo
carry clear/ unsigned lower
C = 0
4
mi
negative/ minus
N = 1
5
pl
positive or zero/ plus
N = 0
6
vs
overflow
V = 1
7
vc
no overflow
V = 0
8
hi
unsigned higher
(C = 1) ∧ (Z = 0)
9
ls
unsigned lower or equal
(C = 0) ∨ (Z = 1)
10
ge
signed greater than or equal
N = 0
11
lt
signed less than
N = 1
12
gt
signed greater than
(Z = 0) ∧ ( N = 0)
13
le
signed less than or equal
(Z = 1) ∨ (N = 1)
14
al
always
15
–
reserved

## Slide 23: Example
Write an ARM assembly program to compute the factorial of a positive
number (> 1) stored in r0. Save the result in r1.
Answer:
ARM assembly
mov r1, #1 /* prod = 1 */
mov r3, #1 /* idx = 1 */
.loop:
mul r1, r3, r1 /* prod = prod * idx */
cmp r3, r0 /* compare idx, with the input (num) */
add r3, r3, #1 /* idx ++ */
bne .loop /* loop condition */

## Slide 24: Branch and Link Instruction
We use the bl instruction for a function call
Semantics
Example
Explanation
bl
label
bl .foo
(1) Jump unconditionally to the function at .foo
(2) Save the next PC (PC + 4) in the lr register

## Slide 25: Example
Example of an assembly program with a function call.
C
int foo() {
return 2;
}
void main() {
int x = 3;
int y = x + foo();
}
ARM assembly
foo:
mov r0, #2
mov pc, lr
main:
mov r1, #3 /* x = 3 */
bl foo /* invoke foo */
/* y = x + foo() */
add r2, r0, r1

## Slide 26: The bx Instruction
This is the preferred method to return from a function.
Instead of : mov pc, lr Use : bx lr
Semantics
Example
Explanation
bx reg
bx r2
(1) Jump unconditionally to the address contained in register, r2

## Slide 27: Example
foo:
mov r0, #2
bx lr
main:
mov r1, #3 /* x = 3 */
bl foo /* invoke foo */
/* y = x + foo() */
add r2, r0, r1

## Slide 28: Conditional Variants of Normal Instructions
Normal Instruction + <condition>
  Examples : addeq, subne, addmi, subpl
Also known as predicated instructions
If the condition is true
  Execute instruction normally
Otherwise
  Do not execute at all

## Slide 29
Write a program in ARM assembly to count the number of 1s in a 32 bit number stored in r1. Save the result in r4.
Answer:
mov r2, #1 /* idx = 1 */
mov r4, #0 /* count = 0 */
/* start the iterations */
.loop:
/* extract the LSB and compare */
and r3, r1, #1
cmp r3, #1
/* increment the counter */
addeq r4, r4, #1
/* prepare for the next iteration */
mov r1, r1, lsr #1
add r2, r2, #1
/* loop condition */
cmp r2, #32
ble .loop

## Slide 30: Outline
Basic Instructions
Advanced Instructions
Branch Instructions
Memory Instructions
Instruction Encoding

## Slide 31: Basic Load Instruction
ldr r1, [r0]
ldr r1, [r0]
r0
r1
register
file
memory

## Slide 32: Basic Store Instruction
str r1, [r0]
str r1, [r0]
r0
r1
register
file
memory

## Slide 33: Memory Instructions with an Offset
ldr r1, [r0, #4]
  r1 ← mem[r0 + 4]
ldr r1, [r0, r2]
  r1 ← mem[r0 + r2]

## Slide 34: Table of Load/Store Instructions
Note the base-scaled-index addressing mode
Semantics
ldr reg, [reg]
ldr reg, [reg, imm]
ldr reg, [reg, reg]
ldr reg, [reg, reg, shift imm]
Example
ldr r1, [r0]
ldr r1, [r0, #4]
ldr r1, [r0, r2]
ldr r1, [r0, r2, lsl #2]
Explanation
r1 ← [r0]
r1 ← [r0 + 4]
r1 ← [r0 + r2]
r1 ← [r0 + r2 << 2]
Addressing Mode
register-indirect
base-offset
base-index
base-scaled-index
str reg, [reg]
str reg, [reg, imm]
str reg, [reg, reg]
str reg, [reg, reg, shift imm]
str r1, [r0]
str r1, [r0, #4]
str r1, [r0, r2]
str r1, [r0, r2, lsl #2]
[r0] ← r1
[r0 + 4] ← r1
[r0 + r2] ← r1
[r0 + r2 << 2] ← r1
register-indirect
base-offset
base-index
base-scaled-index

## Slide 35: Example with Arrays
C
void addNumbers(int a[100]) {
int idx;
int sum = 0;
for (idx = 0; idx < 100; idx++){
sum = sum + a[idx];
}
}
Answer:
ARM assembly
/* base address of array a in r0 */
mov r1, #0 /* sum = 0 */
mov r2, #0 /* idx = 0 */
.loop:
ldr r3, [r0, r2, lsl #2]
add r2, r2, #1 /* idx ++ */
add r1, r1, r3 /* sum += a[idx] */
cmp r2, #100 /* loop condition */
bne .loop

## Slide 36: Advanced Memory Instructions
Consider an array access again
  ldr r3, [r0, r2, lsl #2] /* access array */
  add r2, r2, #1 /* increment index */
Can we fuse both into one instruction
  ldr r3, [r0], r2, lsl #2
  Equivalent to :
    r3 = [r0]
    r0 = r0 + r2 << 2
Post-indexed addressing
mode

## Slide 37
Pre-Indexed Addressing Mode
Consider
  ldr r0, [r1, #4]!
This is equivalent to:
  r0  mem [r1 + 4]
  r1  r1 + 4
Similar to i++ and ++i in Java/C/C++

## Slide 38
C
void addNumbers(int a[100]) {
int idx;
int sum = 0;
for (idx = 0; idx < 100; idx++){
sum = sum + a[idx];
}
}
Answer:
ARM assembly
/* base address of array a in r0 */
mov r1, #0 /* sum = 0 */
add r4, r0, #400 /* set r4 to address of a[100] */
.loop:
ldr r3, [r0], #4
add r1, r1, r3 /* sum += a[idx] */
cmp r0, r4 /* loop condition */
bne .loop
Example with Arrays

## Slide 39: Memory Instructions in Functions
stmfd → spill a set of registers
ldmfd → restore a set of registers
Instruction
Semantics
ldmfd sp!, {list of registers }
stmfd sp!, {list of registers }
Pop the stack and assign values to registers
in ascending order. Update sp.
Push the registers on the stack in descending
order. Update sp.

## Slide 40: Example
Write a function in C and implement it in ARM assembly to compute xn,
where x and n are natural numbers. Assume that x is passed through r0, n
through r1, and the return value is passed back to the original program via
r0. Answer:
ARM assembly
power:
cmp r1, #0 /* compare n with 0 */
moveq r0, #1 /* return 1 */
bxeq lr /* return */
stmfd sp!, {r4, lr} /* save r4 and lr */
mov r4, r0 /* save x in r4 */
sub r1, r1, #1 /* n = n - 1 */
bl power /* recursively call power */
mul r0, r4, r0 /* power(x,n) = x * power(x,n-1) */
ldmfd sp!, {r4, pc} /* restore r4 and return */

## Slide 41: Outline
Basic Instructions
Advanced Instructions
Branch Instructions
Memory Instructions
Instruction Encoding

## Slide 42: Generic Format
Generic Format
cond → instruction condition (eq, ne, … )
type → instruction type
cond
32
29
type
27
28
4
2

## Slide 43: Data Processing Instructions
Data processing instruction type : 00
I → Immediate bit
opcode → Instruction code
S → 'S' suffix bit (for setting the CPSR flags)
rs, rd → source register, destination register
cond
32
29
0 0
27
28
4
2
I
26
4
shifter operand/
immediate
25
22
S
21
4
rs
20
17
rd
4
16
13
12
12
1
opcode

## Slide 44: Encoding Immediate Values
ARM has 12 bits for immediates
  12 bits
What do we do with 12 bits ?
  It is not 1 byte, nor is it 2 bytes
Let us divide 12 bits into two parts
  8 bit payload + 4 bit rot

## Slide 45: Encoding Immediates - II
The real value of the immediate is equal to : payload ror (2 * rot)
The programmer/ compiler writes an assembly instruction with an immediate: e.g. 4
The assembler converts it in to a 12 bit format (if it is possible to do so)
The processor expands 12 bits → 32 bits
rot
payload
4
8

## Slide 46: Encoding Immediates - III
Explanation of encoding the immediate in lay man's terms
  The payload is an 8 bit quantity
  A number is a 32 bit quantity.
  We can set 8 contiguous bits in the 32 bit number while specifying an immediate
  The starting point of this sequence of bits needs to be an even number such as 0, 2, 4, ...

## Slide 47
Examples
Encode the decimal number 42.
Answer:
42 in the hex format is 0x2A, or alternatively 0x 00 00 00 2A. There is no right rotation involved. Hence, the immediate field is 0x02A.
Encode the number 0x2A 00 00 00.
Answer:
The number is obtained by right rotating 0x2A by 8 places. Note that we need to right rotate by 4 places for moving a hex digit one position to the right. We need to now divide 8 by 2 to get 4. Thus, the encoding of the immediate: 0x42A

## Slide 48: Encoding the Shifter Operand
rt
4
4
1
0
5
7
6
shift type
12
8
shift imm
2
5
rt
4
4
1
1
5
7
6
shift type
12
8
shift reg
2
4
9
Shift type
lsl
lsr
asr
ror
00
01
10
11
(a)
(b)
(c)

## Slide 49: Load/Store Instructions
Memory instruction type : 01
rs, rd, shifter operand
  Connotation remains the same
Immediates are not in (rot + payload format) : They are standard 12 bit unsigned numbers
cond
32
29
0 1
27
28
4
2
I
6
shifter operand/
immediate
4
rs
20
17
rd
4
16
13
12
12
1
P
U
B
W
L

## Slide 50: I, P, U, B, W, and L bits
Bit
Value
Semantics
I
0
last 12 bits represent an immediate value
1
last 12 bits represent a shifter operand
P
0
post-indexed addressing
1
pre-indexed addressing
U
0
subtract offset from base
1
add offset to base
B
0
transfer word
1
transfer byte
W
0
do not use pre or post indexed addressing
1
use pre or post indexed addressing
L
0
store to memory
1
load from memory

## Slide 51: Branch Instructions
L bit → Link bit
offset → branch offset (in number of words, similar to SimpleRisc)
offset
32
29
26
28
4
3
L
25
24
101
1
24
cond

## Slide 52: Branch Instructions - II
What does the processor do
  Expands the offset to 32 bits (with proper sign extensions)
  Shifts it to the left by 2 bits (because offset is in terms of memory words)
  Adds it to PC + 8 to generate the branch target
Why, PC + 8 ?
  Read chapter 9

## Slide 53
THE END