## Slide 1
S. Rana
1. Sheet of tufts of 1.5 kg/m is being fed to a cleaner at 12 m/min. A three armed beater is running at 800 rpm. Calculate intensity of opening in g/strike. (2 marks) [Ans: 7.5]
2. A Kirschner beater (with 3 arms) is running at the speed of 800 rpm. A sheet of cotton of 1.2 kg/m is fed by a feed roller (10 cm diameter) running at 10 rpm. Calculate blows /kg on cotton (2 marks) [Ans: 636.6]
3. A multimixer has 8 compartments. Each compartment’s size (H*L*W) is 6 m* 2 m * 0.5 m. The average density of cotton tuft within the compartment is 12 kg/m3. The mixer is filled up in a staggered fashion. (i) What is the capacity of the multimixer? (ii) If time to fill up each box is 5 min, what will be the blending delay time for the first layer of tufts moving out of the machine? (4 marks)[Ans: 324 kg, 140 min].
4. In a blowroom line, a fine cleaner gives cleaning efficiency of 24% for trash content in the feed of 4.3%. The amount of waste collected under the cleaner is 2.8%. Calculate the trash and lint% in the waste ( 4 Marks) [Ans: 40%, 60%].
5. A scutcher is producing a lap of 0.0012 Hk. The delivery speed is 10 m/min. Calculate (i) production/shift at 85% efficiency, (ii) production if the lap hank is made 10% finer, and (iii) % loss in production due to finer lap hank. (4 marks) [Ans: 2001 kg, 1819 kg, 9.1%)
Problems for Practice